## Slide 1: RQ–30 CONTACT FREE DISCHARGE MEASUREMENT SYSTEM

## Slide 2: SOMMER - Information
was founded in 1987 in AUSTRIA and provides more than 30 years experience in development and production of high quality and innovative measurement equipment for hydrology and meteorology.
is a family owned company with excellent reputation. Customer focus, reliability, excellent service and high-end products are our commitment to you.
SOMMER Headquarter is located in west Austria SOMMER production facility
– opened May 2015

## Slide 3
Beginning of the ALPS. Mostly mountainous area. In winter snow covered. Flood danger if snow melt and rain at the same time
Vorarlberg - Austria

## Slide 4: SOMMER - History
started with the production of data logging systems and heavy duty weather station for high alpine conditions.
After getting well known for its robust and high quality ASW, kick-started the development of its snow measurement and analysis systems.
Soon after, developed it´s first generation of contact free discharge measurement Radars and started to promote its product world wide.
SOMMER Snow Pack analyzer and SOMMER SSG installed in Antarctica (South pole). High quality instruments for the roughest conditions.
SOMMER MRS X and MRS 4 data logger
SOMMER ASW in the European Alps
SOMMER RQ-24, first contact free discharge measurement Radar
1987
1990
2005

## Slide 5: SOMMER - History
used it´s specialized knowledge of measuring discharge in rivers and streams to develop a flow meter, for the non contact measurement of waste water, sewage systems and industrial waters, the SQ.
Worldwide distributor network is continuously growing. has distributer in 60 counties of the world on all continents.
After several year of perfecting, start selling it´s unique ice detection system the IDS-20.
opened its first overseas office in Kula Lumpur, Malaysia.
SOMMER SQ-flow meter
2015
2016
2017
SOMMER distributer Network
SOMMER IDS-20 Installed on Wind turbine and at Vienna Airport
2018

## Slide 6: SOMMER – Area of activity
Meteorology – Measurement of different snow parameters and snow melt analysis
Hydrology – Discharge and water level measurement of Rivers and streams Flood warning systems and networks
Sewer and industrial waters – Discharge measurement of open manmade channels and sewer systems
Mining industry – Measurement of water resources in snow and measuring of water flows in the mining process
Ice detection – Detection of ice and ice growth in different industries. (Wind power, Aviation, Power lines communication, Railway,…)

## Slide 7
Meteorology
Snow water equivalent (SWE): SSG – Snow scale
No antifreeze liquid required
Robust aluminum construction
Range from 200 to 3000 mm SWE
Snow Depth: USH-9
Maintenance free ceramic Membrane
Integrated Temp. compensation
High power pulse for best results during snowfall
SWE + ice and water contend: SPA– Snow pack analyzer
Prediction of runoff
No ice bridging effect
SWE, snow-depth, snow density, liquid water and ice contend
Snow melting (Runoff): SMA-Snow melt analyzer
Prediction of runoff
Simple and easy installation
SWE, snow density, liquid water and ice contend close to the ground
Monitor environment: AWS – Automatic Weather station
Heavy duty weather station for high alpine areas
More than 30 years experience
Complete system out of one hand (Steel construction, sensors, software and know how)
Ice risk detection: IDS 20 – Ice detection sensor
Internal plausibility check (dew point/frost point , temp.)
Easy integration in existing systems
Different sensors for different applications (Airports, Antennas in mountain areas, power lines, wind turbines)
Snow Ice measurement sensors:

## Slide 8: What instrument can you use here?

## Slide 9: What instrument can you use here?

## Slide 10: Rhine (Lustenau May 2016)

## Slide 11
Non-Contact Radar Sensors
Tracer Dilution Method
Stationary RQ-30
Mobile RP-30
Mobile TQ-S / TQ-F
SOMMER – Discharge measurement

## Slide 12
Hydrology
SOMMER is the global leading None contact radar based solution provider for measuring discharge
and has more then 15years expiriance
in applications
all arround the world with 1000 nd‘s of units
installed arround the globe.
SOMMER developed
a special complex
model revolutiionising and
making it to the most advanced
company in measurinig
contact free discharge and flow.

## Slide 13: Non-Contact discharge Sensor - RQ-30
SOMMER - Hydrology

## Slide 14
Advantages of Contact free discharge measurement with RQ-30
Contact free measurement
Easy mounting and installation
! Maintenance free (because not in the water)
  High reliability at floods
  No damage of sensor by flotsam, trees, debris, bed load,…
  Discharge calculation in the sensor
Contact free discharge measurement

## Slide 15: RQ-30 Measurement principle
SOMMER - Hydrology

## Slide 16
Water level (stage)
Transit time measurement
Radar (26 GHz) Vertical to water surface
Time between transmitting and reflecting the pulse = directly proportional to the distance
Radar: independent of air temperature and medium (e.g. foam)
RQ-30 Water level sensor
Notes: The Water Level is measured through transit Time method. The Level sensor can be ultrasonic or radar technology. The Radar technology as a couple of advantages like, it is not influenced by the temperature and by foam on the water.
The Velocity in measured with Doppler frequency shift method and only comes as Radar technology. Because the Doppler frequency shift is a physical phenomena the velocity measuring is very accurate.

## Slide 17
Flow velocity
Measurement of Doppler frequency shift (Doppler Effect)
Radar impulse (24 GHz) are shifted by the water surface waves
Frequency shift by movement on the water surface (min. swell 3mm )
Measurement of surface velocity, calculation of mean velocity with hydraulic model
Certified velocity measurement by METAS
RQ-30 Velocity sensor
Notes: The Water Level is measured through transit Time method. The Level sensor can be ultrasonic or radar technology. The Radar technology as a couple of advantages like, it is not influenced by the temperature and by foam on the water.
The Velocity in measured with Doppler frequency shift method and only comes as Radar technology. Because the Doppler frequency shift is a physical phenomena the velocity measuring is very accurate.

## Slide 18: RQ-30 / SQ-Series Measurement Principle
Notes: The RQ measure the water level. With the level and the river profile we calculate the wet area of the cross section of the river. The RQ also measure a local surface velocity. With our hydraulic model we calculate the relation between the local surface velocity and mean velocity at different stages.
The hydraulic model is based on modified equations from Manning and Strickler.
Mean velocity multiply by the wet area is the discharge.

## Slide 19
Discharge (Q)
cross section profile
Continuity Equation:
Q = vm * A(W)
water level measurement
Vm = Vl * k
mean velocity vm
k Factor
RQ-30 Discharge calculation
cross section
Local velocity vl
k-Factor
Area A (W)
Mean velocity
Discharge Q
Defined (Q-Commander)
Measured from Sensor
Calculated by sensor
Water level
local velocity vl measurement
water area A(W)
Notes: The SQ measures the Level an the Velocity.
Then the sensor take the Cross section profile and calculate together with the water level the wetted area A(w).
After the SQ take the local velocity and the k-factors and calculate the mean velocity. The K-factors are coming form our hydraulic model and will be transfer to the SQ during the installation of the sensor.
The K-factors are related to the cross section profile shape, the water level and the roughness of the cross section profile .
After this 2 calculations the SQ will take the wetted area and the mean velocity and calculate the discharge in real-time.

## Slide 20: Compare with Conventional Discharge Measurement (Water level measurement with rating curve)
SOMMER - Hydrology

## Slide 21
Water level sensor with Rating Curve
Investment costs look lower (but operation cost are high)
Need Rating curve to calculate discharge
  Good rating curve need up to 2 years to create
  Very expensive equipment necessary to crate rating curve (current meter, ADCP boats)
  No accurate flood measurement (rating curve need to be calculated)
Only water level information to get to the discharge
  No information about velocity change
If riverbed change, NEW rating curve necessary !!
Flood waring only with water level
NO information about the real flow
RQ-30 Method
Same infrastructure and same RTU station
Calculates discharge in the sensor
  Discharge right after the installation available
  NO reference measurements necessary (but possible)
  Reliable Measurement even during floods
Water level and velocity to calculate accurate discharge
  Detection of dynamic processes in the water Detection of riverbed change Hysteresis
  …
Input new cross section and DONE
Earlier waring of floods (velocity increase)
Detection of flow stop, blockage and backwater
RQ-30 - Rating curve comparison
Notes: Conclusion:
The Rating curve looks easy and cheap, but to get a good discharge output from the rating curve, a lot of time, manpower and money is necessary.
With the RQ-30 the discharge is evidently available and also deliver more reliable discharge data because the real velocity is measured. The RQ-30 also deliver reliable and repeatable data during floods and high water condition.

## Slide 22
̶̶ ̶ Rating Curve, measurement time 2 years
 RQ-30, measurement time 1 month
From here Rating curve is calculated
River went over the banks
RQ-30 - Rating curve comparison
Notes: It took very long to generate the red rating curve and the top of the rating curve was extrapolated because in such high water conditions it was not possible to measure the discharge. In a very short time after the RQ installation the RQ proved the rating curve correct ant also monitored a floodwater situation.

## Slide 23: RQ-30 Data set Analysis (Application Examples)
SOMMER - Hydrology
Notes: Now some Application examples.

## Slide 24
Recognition of dynamic processes in the water body The RQ-30 deliver data to detect the following processes in the water body and cross-section.
  Hysteresis
  Change of Riverbed
  Recognition of vegetation
  Change from normal flow to super- or subcritical flow
  Tide effects
RQ-30 - Data set analysis

## Slide 25
Continuous measurement of water level and flow velocity
  Control of quality of measurement and measuring site through generating the discharge curve
Blue = velocity / Red = Water level
RQ-30 - Data set analysis
Notes: This is a perfect example. The Water level cure fits quite exactly together with the velocity curve and the discharge curve. NEXT page the curve is much bigger

## Slide 26
Blue = velocity / Red = Water level
You can see very fast increase an decrease of the water level and velocity.
RQ-30 - Data set analysis
Notes: You can see very fast increase of water level and velocity.

## Slide 27
Rating curve created with the RQ-30
  Perfect rating curve of level and discharge. Very high repeatability.
  Rating curve of level and velocity with small “arms”. This are dynamic effects in the Water, like Hysteresis effect.
Water Level [cm]
Water Level [cm]
Discharge [m³/s]
Velocity [m/s]
RQ-30 - Data set analysis
Notes: The Top is a perfect example of a rating curve in relation between level and discharge. The cure is very narrow and you see the repeatability of the measurement.
In the Bottom right corner is a rating curve in relation between level and velocity you see small arms going out of the curve. This are dynamic effect in the water, like hysteresis.

## Slide 28
Recognition of flow hysteresis
Green = flow velocity / Blue = Water level
RQ-30 - Data set analysis
Notes: What is the Hysteresis effect ? It is a hydraulic phenomenon. When the water level is increasing the flow velocity is faster when the water level is decreasing the flow velocity is slower. That means at the same Water level you can have 2 different velocity's. This you never find out if you only measure from time to time. But because the RQ-30 is stationary he will also monitor this kind of events.

## Slide 29
Green = flow velocity
Blue = Water level
Water level is increasing
Water level is decreasing
At the same water level,
different velocity's
and a different discharge.
RQ-30 - Data set analysis
Notes: What is the Hysteresis effect ? It is a hydraulic phenomenon. When the water level is increasing the flow velocity is faster when the water level is decreasing the flow velocity is slower. That means at the same Water level you can have 2 different velocity's. This you never find out if you only measure from time to time. But because the SQ is stationary he will also monitor this kind of events.

## Slide 30
Rating curve of a river with hysteresis effect.
Water Level [cm]
Discharge [m³/s]
RQ-30 - Data set analysis
Notes: The rating curve not looks like line any more. At rivers like this a stationary discharge measurement is needed to know the exact discharge over a long time period.
At rivers with hysteresis effect you can measure the discharge with the ACDP boat a 2 different time with the same level and you will get 2 different discharges.

## Slide 31
Blue + Green = flow velocity / Black + Red = Water level
Recognition of river bed changes
RQ-30 - Data set analysis

## Slide 32
Before the flood event the black rating curve was measured.
Blue + Green = velocity /
Black + Red = Water level
After the flood event the rating curve has changed to the red one.
Recognition of cross section changes
Flood event
Water Level [cm]
Discharge [m³/s]
RQ-30 - Data set analysis
Notes: After the flood the relation between Discharge and level has changed. This is a indication that the river bed has changed. If the river is only monitored with a level sensor you will not find out that the river bed has changed.

## Slide 33
Recognition of flow characteristic from normal flow to supercritical flow
  What is supercritical flow ? Supercritical flow is when the Velocity increases but the water level stay the same.
RQ-30 - Data set analysis
Notes: What is supercritical flow ? Supercritical flow is when the Velocity increases but the water level stay the same. This happen most likely when the water drop over a ledge.

## Slide 34
Velocity increases but the water level stay the same.
Velocity [m/s]
Water Level [cm]
RQ-30 - Data set analysis
Notes: What is supercritical flow ? Supercritical flow is when the Velocity increases but the water level stay the same. This happen most likely when the water drop over a ledge.

## Slide 35
River with very high vegetal invasion
  Removal of the vegetal invasion during the measurement time range.
Blue = flow velocity / Red = Water level / Green = Discharge
RQ-30 - Data set analysis

## Slide 36
Blue = flow velocity / Red = Water level / Green = Discharge
Water level and Velocity increase and decrease in the same rate
Vegetation starts growing and the water level increase but the velocity gets slower
The vegetation influent the velocity and water level correlation very much. Even though the discharge stayed over the hole period almost the same.
Vegetation was removed
RQ-30 - Data set analysis

## Slide 37
Tidal river in Belgium
  River width~ 50 m
  Reversal of the flow direction due to tide
  Tidal range ~ 4 m
  Installation on bridge railing
Blue = flow velocity / Red = Water level
RQ-30 - Data set analysis
Notes: You can see very nice how the velocity getting positive and negative

## Slide 38
Blue = flow velocity / Red = Water level
Water Level [cm]
Velocity [m/s]
You even can see the influence of the moon
RQ-30 - Data set analysis
Notes: You can see very nice how the velocity getting positive and negative

## Slide 39: Q – Commander software - Parameters

## Slide 40: Q – Commander software - profiles
Diverse profile options
Egg shapes, circle, others
Trapezoid, rectangular

## Slide 41: Q – Commander software - profiles

## Slide 42
Rivers, streams and mountain torrents
  Hydrographic services
  Civil service and protection
  Hydro power plants
Open channels, canals, drains
  Hydro power plants
  Waste water
  Industry
  Irrigation
  Water management
RQ-30 - Applications

## Slide 43
Easy and economic installation
  No installation underwater
  No construction in the river necessary
  Installation all-the-year possible
  Mounting height from 0.5 to 75m
  Independent from flow direction
  Mobile and fixed installation
  Mounting at bridge without drilling
  Safe from vandalism
RQ-30 - Installation

## Slide 44: Multi sensor application RQ-30d
SOMMER - Hydrology

## Slide 45
on wide rivers
above gates
on rivers with different flow characteristics across the surface
Multiple RQ-30d and/or RG-30d on one cross section
Divide the cross section in several vertical sections
Up to 8 devices on one bus
RQ-30d master
RG/RQ-30d slave
RG/RQ-30d slave
For installation:
RQ-30d

## Slide 46
1x Master: RQ-30d
Max. 7x Slaves:
  RG-30d or RQ-30d
For extreme complex scenarios, flexibility is key
  RQ-30dL Master without Level
  RG-30d Slaves
  RL-15/35/75m Level sensors
Every partial discharge will be calculated
Total discharge sum will be outputted
Analog output of total discharge is possible
No averaging of velocity or level
No analog output of partial discharges
RQ-30d - Details

## Slide 47
RQ-30d

## Slide 48
RQ-30d Slave 1 RQ-30d Master RQ-30d Slave 2
RQ-30d
Notes: The Cross section will be separated in parts and the discharge is calculated for each part separately and later added together in the Master unit.

## Slide 49
River width about 240m
complex hydraulic situation:
  Bridge pillar, curve, inflow of an additional river
Measurement with 2 RQ-30d systems and calculation of the complete discharge
Installation on bridge railing
Power supply by solar panel and data transfer per radio
RQ-30d – INN, schärding, Austria

## Slide 50
RQ-30d – INN, schärding, Austria
Notes: River width about 240m
complex hydraulic situation:
Bridge pillar, curve, inflow of an additional river
Measurement with 2 RQ-30 systems and calculation of the complete discharge
Installation am bridge railing
Power supply by solar panel and data transfer per radio

## Slide 51
River width about 240m
complex hydraulic situation:
  Bridge pillar, curve, inflow of an additional river
Measurement with 2 RQ-30d systems and calculation of the complete discharge
Installation on bridge railing
Power supply by solar panel and data transfer per radio
RQ-30d – INN, schärding, Austria

## Slide 52
Comparison of the results
  Measurement 1 (2014)
  RP-30: 912,9 m³/s
  RQ-30d: 911,5 m³/s
  Measurement 2 (2016)
  ADCP-Boat: 684 m³/s
  RP-30: 671 m³/s
  RQ-30d: 680 m³/s
Difference between the measurement results:
  Measurement 1: + 0,15%
  Measurement 2: +0,6% and -1,3%
RQ-30d – INN, schärding, Austria

## Slide 53
RQ-30d – Tainan, Taiwan
Notes: River: Tainan, Taiwan
  Low water ~20 m
  High water ~600 m
Complex hydraulic Situation:
  Curve upstream
  Usually dry river bed
  During tropical storms
  Changes of the water level of 15 m in some hours
Measurement with 2 RQ-30 und 8 RG-30
Power supply with solar panel

## Slide 54
Options
SOMMER - Hydrology

## Slide 55
RQ-30 – ADMS (Automatic discharge measurement station)
  All in one Solution
  RQ-30 + data logger + modem for remote access and read out of data + battery for independent power supply all in one housing
  optional solar panel
RQ-30 - options

## Slide 56: RP-30 Radar Profiler
Mobile discharge measurement form low flow conditions up to flood situations
Hydrology

## Slide 57: RP-30 Features
Measurement of surface velocity profile
Calculation of discharge
  With water level and cross section profile
Portable mobile measurement system
  Wireless data transmission via Bluetooth
  Easy user interface and handling
Application on cable ways, bridge railings and tripods
Contact free discharge measurement
  No danger from flotsam and debris
  Under flood conditions and for high flow velocities

## Slide 58: Application possibilities
Carriage on handrail
On cable way
Tripod

## Slide 59: Rhine - Bangs (Swiss)

## Slide 60: RPCommander

## Slide 61: Jll - Gisingen (Austria)

## Slide 62: Jll - Gisingen (Austria)
Level: | 2.96 m | Discharge 1: | 139.1 m³/s
Area: | 52.3 m² | Discharge 2: | 141.7 m³/s
 |  |  | 140.4 m³/s

## Slide 63: Applications

## Slide 64: Data transmission and handling
SOMMER – Data handling

## Slide 65
Data logger with data transmission and remote access MRL 7
  2G/3G modem
  Data Logger with 80 Chanels/variables
  Solar charge regulator for internal and external battery's
  Backlit display for easy data readout
  Possible to attach a camera
  Logger can be operated fully independently (with batteries or solar-module), no switch cabinet required due to IP 67 rating
RQ-30 - options

## Slide 66
Battery:
In the switch cabinet. Will be charged by the Solar panel and the solar regulator
in the MRL-7
Switch cabinet
Sensors:
Discharge
Level
Precipitation
Turbidity
temperature
Solar Panel
MRL-7 Data logger:
Logs the measurement data
Send data Measurement data via internal mobile internet modem or optional Satellite modem to the customer
Control the charging of the Battery
Satellite modem:
Receive data from MRL-7 compress the data and send it to one of the INMARSAT satellites.
Mobile internet:
Data will be send via terrestrial 2G or 3G mobile internet network
Cell tower:
(By cell operator)
Internet
Internet
Internet
Internet
Inmarsat satellite network
Satellite Ground station
MDS Server:
Receive data and stores data
www.mds.sommer.at :
Web platform to view and download measurement data. Can be accessed from everywhere and several computers.
Metwin.net:
To analyse measurement data. Metwin.net will get data direly automatically from MDS Server. Local computer in the
customer office
Online Data access
www.mds.sommer.at
Service and Maintenance:
Via Mobile internet remotely form the office or at home.
Measurement Station:
Data analysis:
Time laps camera
SOMMER – Data handling

## Slide 67
Benefits of remote access to MRL 7
  Full remote access to SOMMER sensors
    Up to 8 SOMMER sensors with one controller
  Remote Parametrization
  Remote data read out
  Remote side analysis and adjustment
  Connection via SOMMER commander software
Internet
SOMMER – Data handling - logger

## Slide 68
MDS Server (Measured data server)
  SOMMER data hosting service
  easy access to actual data
  Graphical visualisation
  Easy download of data in .csv format
RQ-30 - options

## Slide 69: data processing
>> Download your Demo Metwin version from your MDS account:
mds.sommer.at
Username: demo
Password: sommer

## Slide 70: data processing

## Slide 71
Ccontact free radar measurement  safe and maintenance free
Accurate measurement also in flood condition
Continuous measurement
No fouling
Rating curve Q(h) not required
Recognition of changes in river bed
No limitation with regards to minimum water depth
Fast and easy installation
RQ-30 - summary

## Slide 72: Application Pictures
SOMMER - Hydrology

## Slide 73
Enshi, China
Tirol, Austria
RQ-30 - Applications
China

## Slide 74
Australia
Zimbabwe
USA
RQ-30 - Applications

## Slide 75
Different installations
RQ-30 - Applications

## Slide 76
Tirol, Austria
RQ-30 ADMS, Vorarlberg, Austria
RQ-30 - Applications
Malaysia

## Slide 77
Papa New Guinee
RQ-30 - Applications

## Slide 78
Adana, Turkey
Schwanden, Swiss
RQ-30 - Applications
Brenner, Italy

## Slide 79
Master
Slave
Slave
RQ-30d – Tibet, china

## Slide 80
https://nature.desktopnexus.com/wallpaper/351348/
China, Tibet
RQ-30 - Applications

## Slide 81
TQ – tracer SENSOR
Mobile discharge measurement system
  Wireless data transmission via Bluetooth
  Easy user interface and handling
Calculation of discharge without knowing the cross-section
Tracer can be used where no other method is feasible
Optimal for high velocities and turbulent rivers – but also in “normal” rivers
Based on tracer dilution method
  Different tracers available
  No harm to the environment

## Slide 82
TQ- Amplifier
Laptop
Bluetooth
connection
River
River water for calibration
TQ – TRACER measurement principle

## Slide 83
TQ- Probes
Laptop
Bluetooth
connection
River
Calibration bucket
TQ- Amplifier
TQ – measurement principle

## Slide 84
TQ- Probes
Laptop
Bluetooth
connection
3) Homogenous distribution of tracer at the measurement site. Recording the change of conductivity or fluorescence.
4) Real-time visualization of the measurement and determination of discharge
1) Injection of a known quantity of tracer solution
2) Tracer flows down the river and is well mixed with the water
River
TQ- Amplifier
TQ – measurement principle

## Slide 85: Measurement – Example TQ-S
5 kg NaCl

## Slide 86
Mobile discharge measurement in rivers with unknown cross section
Based on dilution method
Discharge quantity immediately available
Data transmission via Bluetooth with mobile PC
Real-time visualization of results
Simultaneous measurement with up to 4 sensors for increased accuracy and validation of measurement
Optimal for turbulent rivers
TQ – summary

## Slide 87
TQ – applications

## Slide 88: Fish bypasses

## Slide 89
Thank you for your attention!
Further Questions?
Rhine, Vorarlberg
Loisach, Bavaria
Inn, Upper Austria
RQ-30